A - Air
C – Crank/Cable/Chain
D - Derailleur

B - Brakes

Air
Wheel assembly
Know your wheel and tire size, type valve stem (thin Presta or thick Schrader)
- Rim not dented
- Tire; core, cap, sidewalls, and bead.
- Tube protector
- Don’t over pressure quick releases
Tire and tube
- Look to see if valve stem is “clocked” to maker’s name/logo. If not, mark with patch-kit abrasion pad to aid in tire inspection after leak is found.
- If available, use two (2) leavers with a spoke in between them, opposite the valve stem.
- Push tire into the rim bottom to create clearance
- Don’t slice tube.
- Remove tire from rim then remove tube.
- Inspect tube protector strip
- Use leak to know where to inspect tire
- Patch according to directions.
- Reinstall tube in tire “clocked” to the manufacturer’s mark, then the tire, one sidewall at a time on rim. Use leaver if necessary.
Brakes
All
Know your brake type and if possible the group
- Clean rim with dry clean cloth. Use Simple Green etc. if really filthy.
- Pads have even wear, not past wear markings.
- Pads aligned with rim, up/down & if adjustable, slight or no “toe-in”.
- Cable not fraying
Traditional brakes
With brakes applied, minimum 1” between brake arm and handle bar.
Linear Pull/Shimano Vee Brakes
- “Noodle” adjusted to minimum gap required to remove from saddle.
- Check brake pad to rim clearance for 1mm gap. If necessary, use barrel adjuster to obtain 1mm gap between brake pad and rim.
- True rim if it hits brake pads.
“C”
Cables
- Not fraying under pinch bolt
- Brakes pull and release without resistance.
- Shifter cables responsive
Crank-Arms
- Not loose.
- Chain ring not worn.
- Check pedal tightness semi-annually.
Chain
Know your type per number of gears on rear gear cluster.
- Clean
- Properly lubricated
- Not worn
Cassette
Know your gear cluster type, gear count/tooth counts, free wheel or cassette.
- Clean
- Check tooth wear
Derailleur
- Clean
- Adjust limit screws only if:
  - Chain falls off bike.
  - Chain won’t engage outer most gears.
- Use barrel adjuster to fine tune shifting; under or over shift.
- Realign derailleur hanger if shifting jumps gears in middle of range.
- If there is any “hesitation” in shifting, lubricate the cable housing next to the derailleur and if that corrects the problem, replace all cable housing in next full tune-up.

Tools and Their Use

How tight?
Basic Tools

Wye Allen (hex) Wrench & Wye Socket Wrench

Flat Tip & Phillips Tip Screwdrivers | Combination Open End Box End Wrench

Open End Adjustable Wrench
Nice to Have

"Tee" Handle Hex Wrench | Open End Brake Wrench

Cantilever Brake Center Cable 4th Hand Tool

Bike portable pump	~ $20
Patch Kit	~ $5
Tube	~ $8
Tire leavers	~ $4
Multi tool (some have tire leavers)	~ $25
Bag	~ $10
	~ $72

Before Every Ride:
• A • B • C • D •
After Every Ride:
- Inspect tires for glass, gravel shards, and cuts on tread and sidewall
- Check wheels for true
- Clean the bike's mechanical parts as necessary. Once a week or every 200 miles: Lubricate chain (with dry lube; or every other week or 400 miles with wet chain lube).
Tune-up
In general a tune-up involves in-depth cleaning, inspecting, adjusting, lubricating, and minor repair as necessary. This will include minor wheel truing for proper brake operation if it can be done on the bike, chain and cable lubrication. It doesn’t include disassembling the headset, bottom bracket, and wheel hubs. Major wheel truing, parts replacement, i.e chain, brake pads, cables, will be based on rider safety and discussed with the owner prior to the work being accomplished.
Overhaul
In general an over-haul includes disassembling, cleaning, and lubricating the headset, bottom bracket, and wheel hubs. Parts replacement will be discussed with the owner prior to the work being accomplished.
Once a Month:
Completely clean the bike, including the drivetrain if necessary (usually is!)
Inspect chain and freewheel. Measure the chain for wear, check for tight links and replace the chain if necessary
Inspect and lubricate brake levers, derailleurs and all cables
Inspect pedals and lubricate SPD style cleats. Inspect tires for wear; rotate or replace if needed
Inspect and check for looseness in the:
- Stem binder bolt
- Handlebar binder bolt
- Seat post binder bolt (or quick release)
- Seat fixing bolt
- Crank bolts
- Chain-ring bolts
- Derailleur mounting bolts
- Bottle cage bolts
- Rack mounting bolts
- Brake and derailleur cable anchors
- Brake and shifter lever mounting bolts
- Brake mounting bolts
Every Three Months:
- Inspect frame and fork for paint cracks or bulges that may indicate frame or part damage; pay particular attention to all frame joints.
- Visually inspect for bent components: seat rails, seat post, stem, handlebars, chain-rings, crank-arms, brake calipers and brake levers.
Every Six Months:
Inspect and readjust bearings in headset, hubs, pedals and bottom bracket (if possible; some sealed cartridge bearings cannot be adjusted, only replaced).
Annually:
Disassemble and overhaul; replace all bearings (if possible); and remove and if necessary replace all brake and shift cables. This should be performed at 6,000 miles if you ride more than that per year. If you often ride in the rain or mountain bikers who get dirty should overhaul their bicycles more often.

WHEEL SYSTEMS
( ) Dropout alignment checked with alignment tool and adjusted if necessary.
( ) Tires checked for wear, damage, proper mounting and inflation.
( ) Hubs inspected for bent axles.
( ) Cones, races and ball bearings inspected for wear and pits.
( ) Hubs overhauled using new grease.
( ) Hubs adjusted to not be tight or loose.
( ) All hub locknuts secured to 15 - 17ft. lbs. (180 – 204 inch lbs.)
( ) Rims inspected for damage or other work needed.
( ) Major lateral wheel true.
( ) Rims cleaned of lubricant and road grime.
( ) Wheels mounted in proper alignment and security (front axle nuts 180-240 inch lbs.) (rear axle nuts 240-300 inch lbs.) Quick release skewers set so that they require force through the last 90 degrees of closure.
Drive Train Systems
( ) Bottom bracket overhauled using new grease, (if adjustable style) or cartridge style removed & reinstalled using appropriate grease.
( ) Bottom bracket fixed cup secured to 300-360 inch lbs. (when applicable)
( ) Bottom bracket adjusted to not be too tight or to loose.
( ) Visual inspection for straight chainrings.
( ) Crank arms removed, cleaned and reinstalled.
( )Crank arm securely mounted to 390 inch lbs. for square taper and 435 inch lbs. for splined.
( ) Chainring bolts secured to 48-60 inch lbs.
( ) Chain removed, cleaned and lubricated.
( ) Pedals securely mounted to 300-360 inch lbs.
( ) Chain inspected for wear, tight links, twisted links and protruding chain pins.
( ) Chain length checked.
( ) Freewheel/Cassette removed, cleaned and reinstalled.
( ) Freewheel freehub cogs inspected for wear.
( ) Casstte lockring properly secured.
( ) Lubricate chain.
( ) Rear triangle alignment checked.
Brake System
( ) Cable inspected for rust, frays, and kinks in the inner wire and housing.
( ) Cable lubricated where ever they pass through housing.
( ) Brake lever inspected for damage.
( ) Caliper arms and pivot mounting bolts checked for damage.
( ) Brake pads checked for wear and replaced if more than 50 % worn.
( ) Brake pads resurfaced.
( ) If new housing is installed, size to proper length, install housing ferrules and crimp on end caps.
( ) Remove MTB style brakes and grease brake boss.
( ) Brake calipers checked for mounting security. (72-84 inch lbs. for side pull and 24 inch lbs for others)
( ) Adjustable brake pivot adjusted for no play or binding.
( ) Pivot nuts and bolts checked for security.
( ) Brake caliper lubricated at pivots, springs and cable adjusting barrels.
( )Brake lever set to proper alignment and security (strap type 60-72 inch lbs. and cast clamp type 36-60 inch lbs.)
( ) Brake lever pivots, cable anchor pivots and cable adjusters lubricated.
( ) Brake pad height set so as not to rub tire or hit partially below rim.
( ) Pads set parallel to rim.
( ) New pads set with .5mm to 1.5mm toe to reduce squeal.
( ) Pad clearance set to 1-2mm per side (except MTB type).
( ) MTB pad clearance set so that when the pads contact the rim the lever clears the handlebar by minimum of 1 inch.
( ) Cable system stress tested by pulling brake lever firmly a minimum of ten times.
( ) Cable end finished with end cap.
Steering System
( ) Fork inspected for damage.
( ) Headset overhauled using new grease.
Shift System
( ) Derailleur cables inspected for rust, frays, and kinks in the inner wires and housing.
( ) If new housing is installed, size to proper length, install housing ferruels and crimp on end caps.
( ) Cable lubricated wherever the pass through housing.
( ) Cables pre-stressed
( ) Rear derailleur hanger aligned.
( ) Rear derailleur hanger inspected visually for proper alignment.
( ) Rear derailleur inspected for damage, worn jockey wheels and worn pivots.
( ) Rear derailleur removed, cleaned, lubricated and reinstalled.
( ) Rear derailleur pivots, cable adjusters and jockey wheels lubricated.
( ) Rear derailleur mounted securely to 72-84 inch lbs.
( ) Rear derailleur limit screws set to allow shift to largest and smallest sprocket.
( ) Adjust cable tension.
( ) Rear derailleur checked for overshift at all gear combinations.
( ) Front derailleur inspected for damage.
( ) Front derailleur removed, cleaned, lubricated and reinstalled.
( ) Front derailleur pivots lubricated.
( ) Front derailleur checked for proper mounting height and aligned parallel with chainrings.
( ) Front derailleur checked for proper mounting security. (36-60 inch lbs.)
( ) Front derailleur limit screws set for minimum clearance of the derailleur cage to the chain in high and low gear.
( ) Adjust cable tension.
( ) Front derailleur checked for overshift at all gear combinations.
Miscellaneous
( ) Frame checked for damage.
( ) Seat post checked for allowable minimum depth of insertion.
( ) Grease seat post with appropriate grease.
( ) Seat post fixing bolt secured.
( ) Seat checked for proper alignment and security.
( ) Accessories checked for mounting security and interference with moving parts or safety hazards.
( ) Intensive Frame clean and polish.
Test ride
( ) Brakes checked for stopping power and squeal.
( ) Bicycle checked for tracking problems.
( ) Derailleur checked for performance and overshift.
( ) Chain and freewheel cogs checked for skipping under load.
( ) Bicycle checked for unusual noises.