Bicycle Repair Checklist

Model and Color ______________________________________________ Bike Mechanic(s)_________________________________

Please attach all checklists to handlebars for bicycles in progress or completed, please put all tools back when through. Please check off all parts properly adjusted.

- Saddle & Seat Post

- Inspect Saddle for wear

- Grease seat tube if Seat Post doesn’t move freely

- Frame & Fork

- Clean frame and components while feeling for dents, cracks, bends & structurally compromising rust

- Front Tire, Wheel

- Check tire wear, valve angle & cap, inflate to proper PSI

- Ensure wheel is trued

- Rear Tire & Wheel

- Check tire wear, valve angle & cap, inflate to proper PSI

- Ensure wheel is trued

- Front Hub

- Inspect free rotation and bearing play

- Rear Hub

- Inspect free rotation and bearing play

- Front Brakes

- Inspect cables & housings for wear, caps, and ferrules

- Ensure proper cable tension  (tri-flow if needed )

- Ensure wheel is centered in dropout before inspecting if brakes are centered

- Check wear of brake pad, adjust position as needed

- Rear Brakes

- Inspect cables & housings for wear, caps, and ferrules

- Ensure proper cable tension  (tri-flow if needed )

- Ensure wheel is centered in dropout before inspecting if brakes are centered

- Check brake pad for wear, adjust position as needed

- Chain

- Measure length for wear

- lubricate chain

- Freewheel or Cassette

- Inspect for wear (usually is fine if chain is fine)

- Rear Derailleur & Cable

- Inspect Limit Screws alignment

- Cables & housings –wear, rust, bends, caps, ferrules, fraying

- Ensure proper cable tension  (tri-flow if needed )

- Front Derailleur & Cable

- Inspect Limit Screws adjustment

- Cables & housings –wear, rust, bends, caps, ferrules, fraying

- Ensure proper cable tension  (tri-flow if needed )

- Bottom Bracket, Cranks, & Pedals

- Inspect free rotation and bearing play

- Inspect cranks, chain rings for wear

- Headset

- Inspect free rotation and bearing play

- Handlebars, Stem, Grips, & Levers

- Brake levers correct angle (45o )

- Check Handle Bar Grips for wear

- Reflectors – silver front, red rear, and silver wheel spokes

- Put Sticker on Seat Tube (next to cash register)

- Test Ride – Shifts well, brakes aren’t squeaky, nothings loose

- Ready for Inspection by additional volunteer

- Inspected and Approved by __________________

Notes on problems, parts missing, or parts needing replacement